Ptolemy Projects:  The Projection Problem

SPHERICAL EARTH ON FLAT MAPS

Unlike Ptolemy, Samuel Rowbotham (a.k.a. Parallax) argued that Earth is flat
(in his major work, Earth Not A Sphere)

a circular disk with North Pole at center and Antarctica fringing the edge

Flat Earth certainly would make mapping much easier . . .

BUT Earth is spherical  .  .  .  more or less

ellipsoids and geoids

Globe remains highly accurate scale model of Earth, in spite of limitations
	(variation in oblateness and relief less than thickness of paper on common desk globe)

1)	only one-half globe visible at one time

2)	limited by practicality to quite small scales

3)	corollary, not very portable

4)	expensive

FLATTENING THE GLOBE

"Land of Point", a developable surfaces

but Earth  an undevelopable surface

As Ptolemy realized, no way to flatten without distortion (cartoon)

transferring information from globe to flat map — projection

systematic series of parallel, diverging, or converging lines

construction of corresponding grid

number of projections theoretically infinite, but all distort in some fashion or another

DISTORTION

Linear Scale

Linear scale distorted on all maps!  (scale for Mercator projection)

to illustrate, consider simple projection onto tangent plane
			(graphic of projection concept)

degree of distortion expressed by scale factor (SF)

SF =

when SF > 1, map scale is larger than true scale

when SF < 1, map scale is smaller than true scale

Scale factor varies across the map on all projections

BUT nature of variation depends on character of projection
			(as illustrated by other examples)

Scale factor can be determined at a point

AND SF can be different in different directions about a point

as shown by the Squareland example

on the horizontal, SF is 1.0

on the vertical, SF is .5

on the diagonal, SF is .79

Shape and Area

consider meteorite crater on Squareland  .  .  .

on square map, SF is 1.0 in all directions, so circular shape

on projection, SF varies in different directions, and circular
			impact crater becomes an ellipse

a projection on which SF is the same in all directions, from each and every point is
		said to be conformal or orthomorphic

consider the consequences; for example, compare areas of Greenland and
			Mexico; Arabia and Alaska  .  .  .

conformal projections distort area because  .  .  .

scale factor is same in all directions from a point

and constant scale factor cannot be maintained

alternatively, area can be maintained but only by distorting shapes

projections that maintain area are equal area or equivalent

Direction and Angular Relationships

on some projections, rhumb lines are straight

on some projections, some or all straight lines represent great circle arcs

no projection can show both rhumb lines and great circle arcs as
		straight lines

on many projections, straight lines have no special significance

TYPES OF PROJECTIONS:

Over 250 named projections, most derived to meet specific need

some taxonomy necessary

a common and useful approach is to classify by method of projection

geometric or optical projection

azimuthal

conic

cylindrical

mathematical derivation (also termed unique and conventional)